## Slide 1
Nilanjan Byabarta
UEM Kolkata
Quantitative techniques in computer design

## Slide 2: Agenda
* Sample questions on last Slide
measuring and reporting performance

## Slide 3: Performance Measurement
Recall performance is function of
  CPI: cycles per instruction
  Clock cycle
  Instruction count
Reducing any of the 3 factors will lead to improved performance

## Slide 4
Computer performance is the amount of work accomplished by a computer system. The word performance in computer performance means “How well is the computer doing the work it is supposed to do?”. It basically depends on response time, throughput and execution time of a computer system.

## Slide 5
Response time is the time from start to completion of a task. This also includes:
Operating system overhead.
Waiting for I/O and other processes
Accessing disk and memory
Time spent executing on the CPU or execution time.
Throughput is the total amount of work done in a given time.

## Slide 6
CPU execution time is the total time a CPU spends computing on a given task. It also excludes time for I/O or running other programs. This is also referred to as simply CPU time.
Performance is determined by execution time as performance is inversely proportional to execution time.
Performance = (1 / Execution time)
And,
(Performance of A / Performance of B) = (Execution Time of B / Execution Time of A)

## Slide 7
Execution time = CPU clock cycles x clock cycle time
Since clock cycle time and clock rate are reciprocals, so,
Execution time = CPU clock cycles / clock rate
The number of CPU clock cycles can be determined by,
CPU clock cycles = (No. of instructions / Program ) x (Clock cycles / Instruction) = Instruction Count x CPI

## Slide 8
Execution time = Instruction Count x CPI x clock cycle time
= Instruction Count x CPI / clock rate
How to Improve Performance? To improve performance you can either:
Decrease the CPI (clock cycles per instruction) by using new Hardware.
Decrease the clock time or Increase clock rate by reducing propagation delays or by use pipelining.
Decrease the number of required cycles or improve ISA or Compiler.

## Slide 9: A Few Words About Where We Are Headed
Performance = 1 / Execution time simplified to 1 / CPU execution time
CPU execution time = Instructions  CPI / (Clock rate)
Performance = Clock rate / ( Instructions  CPI )
Define an instruction set;
make it simple enough
to require a small number
of cycles and allow high clock rate, but not so simple that we need many instructions, even for very simple tasks
Design hardware
for CPI = 1; seek improvements with CPI > 1
Design ALU for arithmetic & logic ops
Try to achieve CPI = 1 with clock that is as high as that for CPI > 1 designs; is CPI < 1 feasible?
Design memory & I/O structures to support ultrahigh-speed CPUs

## Slide 10: Performance Measurement
First step is to apply concept of pipelining to the instruction execution process
  Overlap computations
What does this do?
  Decrease clock cycle
  Decrease effective CPU time compared to original clock cycle

## Slide 11: Introduction
Principles that are useful in design and analysis of computers:
Make the common case fast !
  If a design trade-off is necessary, favor the frequent case (which is often simpler) over the infrequent case.
  For example, given that overflow in addition is infrequent, favor optimizing the case when no overflow occurs.

## Slide 12: Introduction
Typical performance metrics:
  Response time
  Throughput
Speedup of X relative to Y
  Execution timeY / Execution timeX
Execution time
  Wall clock time: includes all system overheads
  CPU time: only computation time

## Slide 13: Objective:
Determine the frequent case.
Determine how much improvement in performance is possible by making it faster.
Amdahl's law can be used to quantify the latter given that we have information concerning the former.

## Slide 14: Amdahl's Law :
  The performance improvement to be gained from using some faster mode of execution is limited by the fraction of the time the faster mode can be used.
  Amdahl's law defines the speedup obtained by using a particular feature:

## Slide 15: Areas of growth
  Two factors:
Fraction enhanced : Fraction of compute time in original machine that can be converted to take advantage of the enhancement.
    Always <= 1.
Speedup enhanced : Improvement gained by enhanced execution mode:
”

## Slide 16
”
Execution time using original machine with enhancement:

## Slide 23
Speedup overall using Amdahl's Law:

## Slide 24: CPU Performance Equation:
  Often it is difficult to measure the improvement in time using a new enhancement directly.
  A second method that decomposes the CPU execution time into three components makes this task simpler.
  CPU Performance Equation:
where, for example, Clock cycle time = 2ns for a 500MHz Clock rate.

## Slide 25: CPU Performance Equation:
  An alternative to "number of clock cycles" is "number of instructions executed" or Instruction Count ( IC ).
  Given both the "number of clock cycles" and IC of a program, the average Clocks Per Instruction ( CPI ) is given by:

## Slide 26: CPU Performance Equation:
  One difficulty: It is difficult to change one in isolation of the others:
Clock cycle time: Hardware and Organization.
CPI: Organization and Instruction set architecture.
Instruction count: Instruction set architecture and Compiler technology.
where IC i represents number of time instruction i is executed in a program and CPI i represents the average number of clock cycles for instruction i.
Why isn't CPI i a constant

## Slide 27: (million instruction per second) is NOT an alternative metric to time.

## Slide 28: ISA(Instruction set Architecture)
In computer science, an instruction set architecture (ISA), also called computer architecture, is an abstract model of a computer. A device that executes instructions described by that ISA, such as a central processing unit (CPU), is called an implementation.

## Slide 29
ISA describes the design of a Computer in terms of the basic operations it must support. The ISA is not concerned with the implementation-specific details of a computer. It is only concerned with the set or collection of basic operations the computer must support.

## Slide 30
The ISA defines the types of instructions to be supported by the processor. Based on the type of operations they perform MIPS Instructions are classified into 3 types:
Arithmetic/Logic Instructions: These Instructions perform various Arithmetic & Logical operations on one or more operands.
Data Transfer Instructions: These instructions are responsible for the transfer of instructions from memory to the processor registers and vice versa.
Branch and Jump Instructions: These instructions are responsible for breaking the sequential flow of instructions and jumping to instructions at various other locations, this is necessary for the implementation of functions and conditional statements.

## Slide 31: Instruction Set Architecture
31
Application
Instruction Set Architecture
Implementation
…SPARC MIPS ARM x86 HP-PA IA-64…
Intel Pentium X
AMD K6, Athlon, Opteron
Transmeta Crusoe TM5x00

## Slide 32: Instruction Set Architecture
Strong influence on cost/performance
New ISAs are rare, but versions are not
  16-bit, 32-bit and 64-bit X86 versions
Longevity is a strong function of marketing prowess

## Slide 33: Traditional Issues
Strongly constrained by the number of bits available to instruction encoding
Opcodes/operands
Registers/memory
Addressing modes
Orthogonality
0, 1, 2, 3 address machines
Instruction formats
Decoding uniformity

## Slide 34: Pipelining Concepts
Strategies for improving performance
1 – Use multiple independent data paths accepting several instructions
that are read out at once: multiple-instruction-issue or superscalar
2 – Overlap execution of several instructions, starting the next instruction
before the previous one has run to completion: (super)pipelined
2

## Slide 35: Pipelined Instruction Execution

## Slide 36: Alternate Representations of a Pipeline
Except for start-up and drainage overheads, a pipeline can execute one instruction per clock tick; IPS is dictated by the clock frequency

## Slide 37: Alternate Representations of a Pipeline
Except for start-up and drainage overheads, a pipeline can execute one instruction per clock tick; IPS is dictated by the clock frequency

## Slide 38: 15.2 Pipeline Stalls or Bubbles
First type of data dependency

## Slide 39
Without data forwarding,
three bubbles are needed
to resolve a read-after-write
data dependency
Bubble
Bubble
Bubble
Writes into $8
Reads from $8
Bubble
Bubble
Writes into $8
Reads from $8
Two bubbles, if we assume that a register can be updated and read from in one cycle

## Slide 40: Second Type of Data Dependency
Read-after-load data dependency and its possible resolution through bubble insertion and data forwarding.
Without data forwarding, three (two) bubbles are needed to resolve a read-after-load data dependency

## Slide 41: Introduction
A.1 What is Pipelining?
A.2 The Major Hurdle of Pipelining-Structural Hazards
  Data Hazards
  Control Hazards
A.3 How is Pipelining Implemented
A.4 What Makes Pipelining Hard to Implement?
A.5 Extending the MIPS Pipeline to Handle Multi-cycle Operations

## Slide 42: What Is Pipelining
Laundry Example
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folder” takes 20 minutes
A
B
C
D

## Slide 43: What Is Pipelining
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time

## Slide 44: What Is Pipelining Start work ASAP
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 45: Pipelining Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
What Is Pipelining

## Slide 46: MIPS Without Pipelining
What Is Pipelining
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D

## Slide 47: MIPS Functions
What Is Pipelining
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Instruction Fetch (IF):
Send out the PC and fetch the instruction from memory into the instruction register (IR); increment the PC by 4 to address the next sequential instruction.
IR holds the instruction that will be used in the next stage.
NPC holds the value of the next PC.
Passed To Next Stage
IR <- Mem[PC]
NPC <- PC + 4

## Slide 48: MIPS Functions
What Is Pipelining
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Instruction Decode/Register Fetch Cycle (ID):
Decode the instruction and access the register file to read the registers.
The outputs of the general purpose registers are read into two temporary registers (A & B) for use in later clock cycles.
We extend the sign of the lower 16 bits of the Instruction Register.
Passed To Next Stage
A <- Regs[IR6..IR10];
B <- Regs[IR10..IR15];
Imm <- ((IR16) ##IR16-31

## Slide 49: MIPS Functions
What Is Pipelining
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Passed To Next Stage
A <- A func. B
cond = 0;
Execute Address Calculation (EX):
We perform an operation (for an ALU) or an address calculation (if it’s a load or a Branch).
If an ALU, actually do the operation. If an address calculation, figure out how to obtain the address and stash away the location of that address for the next cycle.

## Slide 50: MIPS Functions
What Is Pipelining
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Passed To Next Stage
A = Mem[prev. B]
or
Mem[prev. B] = A
MEMORY ACCESS (MEM):
If this is an ALU, do nothing.
If a load or store, then access memory.

## Slide 51: MIPS Functions
What Is Pipelining
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Passed To Next Stage
Regs <- A, B;
WRITE BACK (WB):
Update the registers from either the ALU or from the data loaded.

## Slide 52: The Basic Pipeline For MIPS
Latches between each stage provide pipelining.

## Slide 53: The Basic Pipeline For MIPS
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
I
n
s
t
r.
O
r
d
e
r
Figure 3.3

## Slide 54: Pipeline Hurdles
Limits to pipelining: Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: HW cannot support this combination of instructions (single person to fold and put clothes away)
  Data hazards: Instruction depends on result of prior instruction still in the pipeline (missing sock)
  Control hazards: Pipelining of branches & other instructions that change the PC
  Common solution is to stall the pipeline until the hazard is resolved, inserting one or more “bubbles” in the pipeline
A.1 What is Pipelining?
A.2 The Major Hurdle of Pipelining-Structural Hazards
-- Structural Hazards
  Data Hazards
  Control Hazards
A.3 How is Pipelining Implemented
A.4 What Makes Pipelining Hard to Implement?
A.5 Extending the MIPS Pipeline to Handle Multi-cycle Operations

## Slide 55: Pipeline Hurdles
Definition
conditions that lead to incorrect behavior if not fixed
Structural hazard
  two different instructions use same h/w in same cycle
Data hazard
  two different instructions use same storage
  must appear as if the instructions execute in correct order
Control hazard
  one instruction affects which instruction is next
Resolution
Pipeline interlock logic detects hazards and fixes them
simple solution: stall ­
increases CPI, decreases performance
better solution: partial stall ­
some instruction stall, others proceed better to stall early than late

## Slide 56: Structural Hazards
When two or more different instructions want to use same hardware resource in same cycle
e.g., MEM uses the same memory port as IF as shown in this slide.
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg

## Slide 57: Structural Hazards
This is another way of looking at the effect of a stall.
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble

## Slide 58: Structural Hazards
This is another way to represent the stall we saw on the last few pages.

## Slide 59: Structural Hazards
Dealing with Structural Hazards
Stall
low cost, simple
Increases CPI
use for rare case since stalling has performance effect
Pipeline hardware resource
useful for multi-cycle resources
good performance
sometimes complex e.g., RAM
Replicate resource
good performance
increases cost (+ maybe interconnect delay)
useful for cheap or divisible resources

## Slide 60: Structural Hazards
Structural hazards are reduced with these rules:
Each instruction uses a resource at most once
Always use the resource in the same pipeline stage
Use the resource for one cycle only
Many RISC ISA’a designed with this in mind
Sometimes very complex to do this. For example, memory of necessity is used in the IF and MEM stages.
Some common Structural Hazards:
Memory - we’ve already mentioned this one.
Floating point - Since many floating point instructions require many cycles, it’s easy for them to interfere with each other.
Starting up more of one type of instruction than there are resources. For instance, the PA-8600 can support two ALU + two load/store instructions per cycle - that’s how much hardware it has available.

## Slide 61: Data Hazards
These occur when at any time, there are instructions active that need to access the same data (memory or register) locations.
Where there’s real trouble is when we have:
instruction A
instruction B
and B manipulates (reads or writes) data before A does. This violates the order of the instructions, since the architecture implies that A completes entirely before B is executed.
A.1 What is Pipelining?
A.2 The Major Hurdle of Pipelining-Structural Hazards
-- Structural Hazards
  Data Hazards
  Control Hazards
A.3 How is Pipelining Implemented
A.4 What Makes Pipelining Hard to Implement?
A.5 Extending the MIPS Pipeline to Handle Multi-cycle Operations

## Slide 62: Data Hazards
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by a “Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
Execution Order is:
InstrI
InstrJ
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 63: Data Hazards
Write After Read (WAR) InstrJ tries to write operand before InstrI reads i
  Gets wrong operand
  Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5
Execution Order is:
InstrI
InstrJ
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 64: Data Hazards
Write After Write (WAW) InstrJ tries to write operand before InstrI writes it
  Leaves wrong result ( InstrI not InstrJ )
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Writes are always in stage 5
Will see WAR and WAW in later more complicated pipes
Execution Order is:
InstrI
InstrJ
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 65: Data Hazards
Simple Solution to RAW
Hardware detects RAW and stalls
Assumes register written then read each cycle
  + low cost to implement, simple
  -- reduces IPC
Try to minimize stalls
Minimizing RAW stalls
Bypass/forward/short­circuit (We will use the word “forward”)
Use data before it is in the register
  + reduces/avoids stalls
  -- complex
Crucial for common RAW hazards

## Slide 66: Data Hazards
The use of the result of the ADD instruction in the next three instructions causes a hazard, since the register is not written until after those instructions read it.
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 67: Data Hazards
Forwarding To Avoid
Data Hazard
Forwarding is the concept of making data available to the input of the ALU for subsequent instructions, even though the generating instruction hasn’t gotten to WB in order to write the memory or registers.
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 68: Data Hazards
There are some instances where hazards occur, even with forwarding.
The data isn’t loaded until after the MEM stage.
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 69: Data Hazards
There are some instances where hazards occur, even with forwarding.
The stall is necessary as shown here.
Time (clock cycles)
or r8,r1,r9
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg

## Slide 70: Data Hazards
This is another representation of the stall.
LW R1, 0(R2) | IF | ID | EX | MEM | WB |  |  | 
SUB R4, R1, R5 |  | IF | ID | EX | MEM | WB |  | 
AND R6, R1, R7 |  |  | IF | ID | EX | MEM | WB | 
OR R8, R1, R9 |  |  |  | IF | ID | EX | MEM | WB
LW R1, 0(R2) | IF | ID | EX | MEM | WB |  |  |  | 
SUB R4, R1, R5 |  | IF | ID | stall | EX | MEM | WB |  | 
AND R6, R1, R7 |  |  | IF | stall | ID | EX | MEM | WB | 
OR R8, R1, R9 |  |  |  | stall | IF | ID | EX | MEM | WB

## Slide 71: Data Hazards
Instruction scheduled by compiler - move instruction in order to reduce stall.
  lw Rb, b ­­ code sequence for a = b+c before scheduling
  lw Rc, c
  Add Ra, Rb, Rc ­­ stall
  sw a, Ra
  lw Re, e ­­ code sequence for d = e+f before scheduling
  lw Rf, f
  sub Rd, Re, Rf ­­ stall
  sw d, Rd
Arrangement of code after scheduling.
  lw Rb, b
  lw Rc, c
  lw Re, e
  Add Ra, Rb, Rc
  lw Rf, f
  sw a, Ra
  sub Rd, Re, Rf
  sw d, Rd
Pipeline Scheduling

## Slide 72: Data Hazards
Pipeline Scheduling

## Slide 73: Control Hazards
A control hazard is when we need to find the destination of a branch, and can’t fetch any new instructions until we know that destination.
A.1 What is Pipelining?
A.2 The Major Hurdle of Pipelining-Structural Hazards
-- Structural Hazards
  Data Hazards
  Control Hazards
A.3 How is Pipelining Implemented
A.4 What Makes Pipelining Hard to Implement?
A.5 Extending the MIPS Pipeline to Handle Multi-cycle Operations

## Slide 74: Control Hazard on Branches Three Stage Stall
Control Hazards
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 75: Branch Stall Impact
If CPI = 1, 30% branch, Stall 3 cycles => new CPI = 1.9!
    (Whoa! How did we get that 1.9???)
Two part solution to this dramatic increase:
  Determine branch taken or not sooner, AND
  Compute taken branch address earlier
MIPS branch tests if register = 0 or ^ 0
MIPS Solution:
  Move Zero test to ID/RF stage
  Adder to calculate new PC in ID/RF stage
    must be fast
    can't afford to subtract
    compares with 0 are simple
    Greater-than, Less-than test sign­bit, but not-equal must OR all bits
    more general compares need ALU
  1 clock cycle penalty for branch versus 3
In the next chapter, we’ll look at ways to avoid the branch all together.
Control Hazards

## Slide 76: Five Branch Hazard Alternatives
#1: Stall until branch direction is clear
#2: Predict Branch Not Taken
  Execute successor instructions in sequence
  “Squash” instructions in pipeline if branch actually taken
  Advantage of late pipeline state update
  47% MIPS branches not taken on average
  PC+4 already calculated, so use it to get next instruction
#3: Predict Branch Taken
  53% MIPS branches taken on average
  But haven’t calculated branch target address in MIPS
    MIPS still incurs 1 cycle branch penalty
    Other machines: branch target known before outcome
Control Hazards

## Slide 77
#4: Execute Both Paths
#5: Delayed Branch
  Define branch to take place AFTER a following instruction
  branch instruction sequential successor1 sequential successor2 ........ sequential successorn
  branch target if taken
  1 slot delay allows proper decision and branch target address in 5 stage pipeline
  MIPS uses this
Branch delay of length n
Control Hazards
Five Branch Hazard Alternatives

## Slide 78: Delayed Branch
Where to get instructions to fill branch delay slot?
  Before branch instruction
  From the target address: only valuable when branch taken
  From fall through: only valuable when branch not taken
  Cancelling branches allow more slots to be filled
Compiler effectiveness for single branch delay slot:
  Fills about 60% of branch delay slots
  About 80% of instructions executed in branch delay slots useful in computation
  About 50% (60% x 80%) of slots usefully filled
Delayed Branch downside: 7-8 stage pipelines, multiple instructions issued per clock (superscalar)
Control Hazards

## Slide 79: Evaluating Branch Alternatives
Scheduling Branch CPI speedup v. Speedup v.
scheme penalty unpipelined stall
Stall pipeline 3 1.42 3.5 1.0
Predict taken 1 1.14 4.4 1.26
Predict not taken 1 1.09 4.5 1.29
Delayed branch 0.5 1.07 4.6 1.31
Conditional & Unconditional = 14%, 65% change PC
Control Hazards

## Slide 80: Pipelining Introduction Summary
Just overlap tasks, and easy if tasks are independent
Speed Up Š Pipeline Depth; if ideal CPI is 1, then:
Hazards limit performance on computers:
  Structural: need more HW resources
  Data (RAW,WAR,WAW): need forwarding, compiler scheduling
  Control: delayed branch, prediction
Speedup =
Pipeline Depth
1 + Pipeline stall CPI
X
Clock Cycle Unpipelined
Clock Cycle Pipelined
Control Hazards

## Slide 81: Compiler “Static” Prediction of Taken/Untaken Branches
Always taken
Taken backwards
Not Taken Forwards
Control Hazards
The compiler can program what it thinks the branch direction will be. Here are the results when it does so.

## Slide 82: Compiler “Static” Prediction of Taken/Untaken Branches
Improves strategy for placing instructions in delay slot
Two strategies
  Backward branch predict taken, forward branch not taken
  Profile-based prediction: record branch behavior, predict branch based on prior run
Control Hazards

## Slide 83: Evaluating Static Branch Prediction Strategies
Misprediction ignores frequency of branch
“Instructions between mispredicted branches” is a better metric
Control Hazards

## Slide 84: What Makes Pipelining Hard?
A.1 What is Pipelining?
A.2 The Major Hurdle of Pipelining-Structural Hazards
  Data Hazards
  Control Hazards
A.3 How is Pipelining Implemented
A.4 What Makes Pipelining Hard to Implement?
A.5 Extending the MIPS Pipeline to Handle Multi-cycle Operations

## Slide 85: What Makes Pipelining Hard?
Examples of interrupts:
Power failing,
Arithmetic overflow,
I/O device request,
OS call,
Page fault
Interrupts (also known as: faults, exceptions, traps) often require
surprise jump (to vectored address)
linking return address
saving of PSW (including CCs)
state change (e.g., to kernel mode)
Interrupts cause great havoc!
There are 5 instructions executing in 5 stage pipeline when an interrupt occurs:
How to stop the pipeline?
How to restart the pipeline?
Who caused the interrupt?

## Slide 86: What Makes Pipelining Hard?
Interrupts cause great havoc!
What happens on interrupt while in delay slot ?
Next instruction is not sequential
solution #1: save multiple PCs
Save current and next PC
Special return sequence, more complex hardware
solution #2: single PC plus
Branch delay bit
PC points to branch instruction
Stage Problem that causes the interrupt
IF Page fault on instruction fetch; misaligned memory access; memory-protection violation
ID Undefined or illegal opcode
EX Arithmetic interrupt
MEM Page fault on data fetch; misaligned memory access; memory-protection violation

## Slide 87: What Makes Pipelining Hard?
Simultaneous exceptions in more than one pipeline stage, e.g.,
  Load with data page fault in MEM stage
  Add with instruction page fault in IF stage
  Add fault will happen BEFORE load fault
Solution #1
  Interrupt status vector per instruction
  Defer check until last stage, kill state update if exception
Solution #2
  Interrupt ASAP
  Restart everything that is incomplete
Another advantage for state update late in pipeline!
Interrupts cause great havoc!

## Slide 88: What Makes Pipelining Hard?
Here’s what happens on a data page fault.
1 2 3 4 5 6 7 8 9
i F D X M W
i+1 F D X M W <­ page fault
i+2 F D X M W <­ squash
i+3 F D X M W <­ squash
i+4 F D X M W <­ squash
i+5 trap ­> F D X M W
i+6 trap handler ­> F D X M W
Interrupts cause great havoc!

## Slide 89: What Makes Pipelining Hard?
Complex Addressing Modes and Instructions
Address modes: Autoincrement causes register change during instruction execution
  Interrupts? Need to restore register state
  Adds WAR and WAW hazards since writes are no longer the last stage.
Memory-Memory Move Instructions
  Must be able to handle multiple page faults
  Long-lived instructions: partial state save on interrupt
Condition Codes
Complex Instructions

## Slide 90: Handling Multi-cycle Operations
Multi-cycle instructions also lead to pipeline complexity.
A very lengthy instruction causes everything else in the pipeline to wait for it.
A.1 What is Pipelining?
A.2 The Major Hurdle of Pipelining-Structural Hazards
  Data Hazards
  Control Hazards
A.3 How is Pipelining Implemented
A.4 What Makes Pipelining Hard to Implement?
A.5 Extending the MIPS Pipeline to Handle Multi-cycle Operations

## Slide 91: Multi-Cycle Operations
Floating point gives long execution time.
This causes a stall of the pipeline.
It’s possible to pipeline the FP execution unit so it can initiate new instructions without waiting full latency. Can also have multiple FP units.
FP Instruction Latency Initiation Rate
Add, Subtract 4 3
Multiply 8 4
Divide 36 35
Square root 112 111
Negate 2 1
Absolute value 2 1
FP compare 3 2
Floating Point

## Slide 92: Floating Point
Divide, Square Root take ­10X to ­30X longer than Add
  Interrupts?
  Adds WAR and WAW hazards since pipelines are no longer same length
Multi-Cycle Operations
Notes:
I + 2: no WAW, but this complicates an interrupt
I + 4: no WB conflict
I + 5: stall forced by structural hazard
I + 6: stall forced by in-order issue

## Slide 93: Summary of Pipelining Basics
Hazards limit performance
  Structural: need more HW resources
  Data: need forwarding, compiler scheduling
  Control: early evaluation & PC, delayed branch, prediction
Increasing length of pipe increases impact of hazards; pipelining helps instruction bandwidth, not latency
Interrupts, Instruction Set, FP makes pipelining harder
Compilers reduce cost of data and control hazards
  Load delay slots
  Branch delay slots
  Branch prediction

## Slide 94: Summary
A.1 What is Pipelining?
A.2 The Major Hurdle of Pipelining-Structural Hazards
  Data Hazards
  Control Hazards
A.3 How is Pipelining Implemented
A.4 What Makes Pipelining Hard to Implement?
A.5 Extending the MIPS Pipeline to Handle Multi-cycle Operations

## Slide 95
Define pipeline chaining
Illustrate thedifferences between dynamic pipeline and static pipeline
Define speedup. Is this speed up always achievable
Demonstrate different factors that can affect the performance of a pipelined system
Differentiate between WAR and RAW with a suitable example.
Evaluate what is meant by pipeline stall
Instruction execution throughput increases in proportion with the number of pipeline stages.” Is it true? Justify your statement.
Construct different approaches taken by pipeline processor to handle branch instructions
Demonstrate branch hazard
Discuss briefly two approaches to handle branch hazards.
State the major hurdles to achieve ideal speed-up
Discuss data hazard briefly.
Write short notes on the following : Pipeline hazards, Branch handling in instruction pipeline.
Explain static and dynamic pipeline with a proper diagram. State the differences between them
Define speedup. Deduce the equation to calculate maximum speed up. Analyze if maximum speed up is always achievable
Discuss the meaning of clock period of a pipeline.State the process to calculate the clock period of a pipeline
Discuss the meaning of frequency and throughput of a pipeline. Deduce the equation when maximum throughput is equal to the frequency of the pipeline.
Explain different techniques for resolving structural hazards.
"Explain how control hazard occurs while executing the following block of code:
10: BEQ R1,R3,36
16: AND R2,R3,R5
22: OR R6,R1,R7
28: ADD R8,R1,R9
36: XOR R10,R1,R11"
Discuss the meaning of operand forwarding and bypassing. State how does it help to solve RAW hazards. Explain with the help of a diagram.